## Pros and Cons of Water Clarification Methods

| Method | Positive Factors | Negative Factors |
| --- | --- | --- |
| Cloth filtration | Free Can be done in a few minutes | Does not remove fine particulates, so need to use double chlorine dose |
| Sand filtration | Can be done in a few minutes | Sand must be changed/cleaned on a regular basis to maintain effectiveness of filter Must buy filter or supplies to build filter Need proper sand, sand must be clean, sand must be graded |
| Settling and Decanting | Free – (except for the cost of one container to use for letting the water sit and a second container to use for pouring the clear water) Pretreating very turbid waters before filtration can increase the number of times a filter can be used before it needs to be cleaned/replaced | Takes up to 12 hours to allow water to settle adequately Not effective on some turbid waters with very fine particles |
| Flocculants | Removes fine particulates so that only a single dose of chlorine is necessary Takes about 35 minutes (which is less time than settling and decanting) | Commercially available flocculants cost money Takes time (100 stirs) and requires “equipment” (stirring stick, water container) Organic flocculants (like moringa seed and racket) cannot be used with chlorine or a chlorine product (such as PUR, Aquasafe, Aquatabs, etc.) |