Minimum Quality Standards for Latrine Construction Given the limited economic resources of the average family, hardware for sanitation and hygiene should be selected with a focus on “appropriate technologies” that are locally sustainable and have an impact on protecting health. The generally accepted definition of “sanitation coverage” requires that a household have access to a sealed, cleaned, and maintained latrine. “Sealed” means that there are covers for the hole in the slab and that any ventilation pipe is screened. This is a minimum standard for a pit latrine. Improved traditional pit latrines meet these minimum standards and may be the most appropriate design in many settings. Sanitation systems should not be constructed that contaminate ground or surface water or otherwise compromise human health or environmental quality. The construction of systems that dispose of raw sewage into a surface water source or into groundwater is not permitted. All latrines, household or institutional, should have access to a hand washing station with sufficient water for multiple hand washings and a cleansing agent (soap, ash, sand). Appropriate low-cost hardware for hand washing that consumes little water is easily furnished (see session on tippy taps) or locally available. Institutional latrines and toilets that see high usage (compared to the household latrine) should maintain minimum standards for a pit latrine, but must also have a slab that is easily covered and cleaned—concrete SanPlats (sanitation platforms) are a low-cost and reasonable technology. The use of local materials to build slabs and superstructures is encouraged as a strategy to reduce or eliminate external subsidies. Adverse conditions for construction of pit latrines (high groundwater tables, soils that cannot be excavated, or soils that collapse easily) limit low-cost options for sanitation and may require a program to offer subsidies for adequate feces disposal options. Selected information adapted from: Training Manual on Hygiene and Sanitation Promotion and Community Mobilization for Volunteer Health Promoters. USAID/HIP.